## Slide 1: Introduction to SNMP
Network Management Workshop
Kuala Lumpur
APRICOT 2010

## Slide 2: Overview
What is SNMP ?
OIDs
MIBs
Polling and querying
Traps

## Slide 3: What is SNMP ?
SNMP – Simple Network Management Protocol
  Industry standard, hundreds of tools exist to exploit it
  Present on any decent network equipment
Query – response based
  GET / SET
    Mostly GET is used for monitoring
Tree hierarchy
  Query for ”Object Identifiers” (OIDs)
Concept of MIBs (Management Information Base)
  Standard and vendor-specific (Enterprise)

## Slide 4: What is SNMP ?
UDP protocol, port 161
Different versions
  Originally, 1988
  v1 – RFC1155, RFC1156, RFC1157
    Original specification
  v2 – RFC1901 ... RFC1908 + RFC2578
    Extends v1, new data types, better retrieval methods (GETBULK)
    Really is version v2c (without security model)
  v3 – RFC3411 ... RFC3418
Typically we use SNMPv2
Terminology:
  Manager (the monitoring ”client”)
  Agent (running on the equipment/server)

## Slide 5: What is SNMP ?
Typical queries
  Bytes In/Out on an interface, errors
  CPU load
  Uptime
  Temperature
  ...
For hosts (servers or workstations)
  Diskspace
  Installed software
  Running processes
  ...
Windows and UNIX have SNMP

## Slide 6: How does it work ?
Basic commands
  GET (manager -> agent)
    Query for a value
  GET-NEXT (manager -> agent)
    Get next value (list of values for a table)
  GET-RESPONSE (agent -> manager)
    Response to GET/SET, or error
  SET (manager -> agent)
    Set a value, or perform action
  TRAP (agent -> manager)
    Spontaneous notification from equipment (line down, temperature above threshold, ...)

## Slide 7: The MIB tree
root
ccitt(0)
iso(1)
joint-iso-ccitt(3)
org(3)
dod(6)
internet(1)
directory(1)
mgmt(2)
1.3.6.1
experimental(3)
private(4)
enterprises(1)
cisco(9)
mib-2(1)
system(1)
interfaces(2)
ip(4)
snmp(11)
host(25)
hrStorage
hrSystem
hrDevice

## Slide 8: The MIB tree
root
ccitt(0)
iso(1)
joint-iso-ccitt(3)
org(3)
dod(6)
internet(1)
directory(1)
mgmt(2)
1.3.6.1
experimental(3)
private(4)
enterprises(1)
cisco(9)
ciscoMgmt(9)
ciscoEnvMonMIB(13)
ciscoEnvMonObjects(1)
ciscoEnvMonTemperatureStatusTable(3)
ciscoEnvMonTemperatureStatusValue(3)
ciscoEnvMonTemperatureStatusEntry(1)
...
mib-2(1)
system(1)
interfaces(2)
ip(4)
snmp(11)

## Slide 9: The Internet MIB
directory(1) OSI directory
mgmt(2) RFC standard objects
experimental(3) Internet experiments
private(4) Vendor-specific
security(5) Security
snmpV2(6) SNMP internal

## Slide 10: OIDs and MIBs
Navigate tree downwards
OIDs separated by '.'
  1.3.6.1.4.1.9. ...
OID corresponds to a label
  .1.3.6.1.2.1.1.5 => sysName
The complete path:
  .iso.org.dod.internet.mgmt.mib-2.system.sysName
How do we convert from OIDs to Labels (and vice versa ?)
  Use of MIBs files!

## Slide 11: MIBs
MIBs are files defining the objects that can be queried, including:
  Object name
  Object description
  Data type (integer, text, list)
MIBS are structured text, using ASN.1
Standard MIBs include:
  MIB-II – (RFC1213) – a group of sub-MIBs
  HOST-RESOURCES-MIB (RFC2790)

## Slide 12: MIBs - 2
MIBs also make it possible to interpret a returned value from an agent
  For example, the status for a fan could be 1,2,3,4,5,6 – what does it mean ?

## Slide 13: MIBs - SAMPLE
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since the
network management portion of the system was last
re-initialized."
::= { system 3 }
sysUpTime OBJECT-TYPE
This defines the object called sysUpTime.
SYNTAX TimeTicks This object is of the type TimeTicks. Object types are specified in the SMI we mentioned a moment ago.
ACCESS read-only This object can only be read via SNMP (i.e., get-request); it cannot be changed (i.e., set-request).
STATUS mandatory This object must be implemented in any SNMP agent.
DESCRIPTION A description of the object
::= { system 3 }
The sysUpTime object is the third branch off of the system object group tree.

## Slide 14: MIBs - SAMPLE
CiscoEnvMonState ::= TEXTUAL-CONVENTION
STATUS current
DESCRIPTION
"Represents the state of a device being monitored.
Valid values are:
normal(1): the environment is good, such as low
temperature.
warning(2): the environment is bad, such as temperature
above normal operation range but not too
high.
critical(3): the environment is very bad, such as
temperature much higher than normal
operation limit.
shutdown(4): the environment is the worst, the system
should be shutdown immediately.
notPresent(5): the environmental monitor is not present,
such as temperature sensors do not exist.
notFunctioning(6): the environmental monitor does not
function properly, such as a temperature
sensor generates a abnormal data like
1000 C.
”

## Slide 15: Querying SNMP agent
Some typical commands for querying:
  snmpget
  snmpwalk
  snmpstatus
Syntax: snmpXXX -c community -v1 host [oid] snmpXXX -c community -v2c host [oid]
Let's take an example
  snmpstatus -c pacn0g2k9 -v1 192.168.1.221
  snmpget -c pacn0g2k9 -v1 192.168.1.223 .iso.org.dod.internet.mgmt.mib-2.interfaces.ifNumber.0
  snmpwalk -c pacn0g2k9 -v1 192.168.1.222 ifDescr

## Slide 16: Querying SNMP agent
Community:
  A ”security” string (password) to define whether the querying manager will have RO (read only) or RW (read write) access
  This is the simplest form of authentication in SNMP
OID
  A value, for example, .1.3.6.1.2.1.1.5.0, or it's name equivalent
  .iso.org.dod.internet.mgmt.mib-2.system.sysName.0
Let's ask for the system's name (using the OID above)
  Why the .0 ? What do you notice ?

## Slide 17: Coming up...
Using snmpwalk, snmpget
Configuring SNMPD
Loading MIBs

## Slide 18: References
Basic SNMP at Cisco http://www.cisco.com/warp/public/535/3.html http://www.cisco.com/univercd/cc/td/doc/cisintwk/ito_doc/snmp.htm
Wikipedia: http://en.wikipedia.org/wiki/Simple_Network_Management_Protocol
IP Monitor MIB Browser http://support.ipmonitor.com/mibs_byoidtree.aspx Cisco MIB browser: http://tools.cisco.com/Support/SNMP/do/BrowseOID.do
Open Source Java MIB Browser http://www.kill-9.org/mbrowse http://www.dwipal.com/mibbrowser.htm (Java)
SNMP Link – collection of SNMP resources http://www.snmplink.org/
Net-SNMP Open Source SNMP tools http://net-snmp.sourceforge.net/