## Slide 1: MRTG and RRDTool
APRICOT 2010 Kuala Lumpur, Malaysia

## Slide 2
Multi Router Traffic Grapher (MRTG)
The Multi Router Traffic Grapher (MRTG) is a tool to monitor the traffic load on network-links.
  MRTG generates HTML pages containing PNG images which provide an almost live visual representation of this traffic. Check http://oss.oetiker.ch/mrtg/ for more information.
  From the mrtg pages: “You have a router, you want to know what it does all day long? Then MRTG is for you. It will monitor SNMP network devices and draw pretty pictures showing how much traffic has passed through each interface.”
Notes: <number>

## Slide 3
MRTG continued
MRTG has been the most common network traffic measurement tool for all Service Providers during this millenium.
MRTG uses simple SNMP queries on a regular interval to generate graphs.
External readers for MRTG graphs can create other interpretation of data.
MRTG software can be used not only to measure network traffic on interfaces, but also build graphs of anything that has an equivalent SNMP MIB - like CPU load, disk availability, temperature, etc...
Data sources can be anything that provides a counter or gauge value – not necessarily SNMP.
  For example, graphing round trip times.
Notes: <number>

## Slide 4
MRTG generates each graph every 5 minutes. This can create considerable overhead if you are graphing for many devices (100’s of routers with multiple interfaces for instance…).
  Example: 500 routers, 2 interfaces each = 1000 graphs to generate. Potential CPU overhead.
Very few customizable graphing options.
MRTG management itself can be tedious work (see next slide…)
MRTG issues
Notes: <number>

## Slide 5
Running MRTG
Install or compile required packages
  apt-get install mrtg
Make cfg files for router interfaces with cfgmaker
Create html pages from the cfg files with indexmaker
Trigger MRTG periodically from cron or run it in daemon mode
Notes: <number>

## Slide 6
MRTG graphs

## Slide 7
RRDtool
Round Robin Database Tool: RRDTool
Round Robin Database for time series data storage
Command line based
From the author of MRTG
Made to be faster and more flexible than using MRTG alone
Includes CGI and Graphing tools, plus APIs: rrdgraph, rrdcreate, rrdtool
Solves the Historical Trends and Simple Interface problems
Notes: <number>

## Slide 8
Define Data Sources (Inputs)‏
When you invoke rrdtool you specify options,
such as these on the command line:
  DS:speed:COUNTER:600:U:U
  DS:fuel:GAUGE:600:U:U
  DS = Data Source
  speed, fuel = “variable” names
  COUNTER, GAUGE = variable type
  600 = heart beat – UNKNOWN returned for interval if nothing received after this amount of time
  U:U = limits on minimum and maximum variable values (U means unknown and any value is permitted)‏
Notes: <number>

## Slide 9
Define Archives (Outputs)‏
RRA:AVERAGE:0.5:1:24
RRA:AVERAGE:0.5:6:10
  RRA = Round Robin Archive
  AVERAGE = consolidation function
  0.5 = up to 50% of consolidated points may be UNKNOWN
  1:24 = this RRA keeps each sample (average over one 5 minute primary sample), 24 times (which is 2 hours worth)‏
  6:10 = one RRA keeps an average over every six 5 minute primary samples (30 minutes), 10 times (which is 5 hours worth)‏
  All depends on original step size which defaults to 5 minutes, i.e. “rrdcreate --step 300”
Was that clear?
Notes: <number>

## Slide 10
Recent data stored once every 5 minutes for the past 2 hours
Medium length data averaged to one entry per half hour for the last 5 hours (6:10)‏
Old data averaged to one entry per
day for the last 365 days (288:365)
--step 300
(5 minute input step size)‏
RRA 1:24
RRA 6:10
RRA 288:365
RRD
File
RRDtool database format
Notes: <number>

## Slide 11
Increasing data granularity
What if you want to keep 5-minute data for an entire year?
How should you specify this?
 RRA:AVERAGE:0.5:1:105120
Where did “105120” come from?
300 seconds = 5 minutes
525600 minutes/year or,
525600/5 = 105120 “300 second intervals” in one year

## Slide 12
rrdtool command line examples
rrdtool create /var/nagios/rrd/host0_load.rrd -s 600 DS:1MIN-Load:GAUGE:1200:0:100 DS:5MIN-Load:GAUGE:1200:0:100 DS:15MIN-Load:GAUGE:1200:0:100 RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800
rrdtool create /var/nagios/rrd/host0_disk_usage.rrd -s 600 DS:root:GAUGE:1200:0:U DS:home:GAUGE:1200:0:U DS:usr:GAUGE:1200:0:U DS:var:GAUGE:1200:0:U RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800
rrdtool create /var/nagios/rrd/apricot-INTL_Ping.rrd -s 300 DS:ping:GAUGE:600:0:U RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800
rrdtool create /var/nagios/rrd/host0_total.rrd -s 300 DS:IN:COUNTER:1200:0:U DS:OUT:COUNTER:600:0:U RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800
Notes: <number>

## Slide 13
Cacti using rrdtool for graphs
Notes: <number>

## Slide 14
RRDTool in the background
Graphs and stores data for tools we use such as:
  Cacti
  Nagios
  Smokeping
  and many more network monitoring packages

## Slide 15
# apt-get install rrdtool
# apt-get install librrdp-perl
# apt-get install librrds-perl
Add in your MRTG Configuration file
  /etc/mrtg/router.mrtg
LogFormat: rrdtool
Run mrtg
Go see in /var/www/mrtg
RRDTool Ubuntu installation
Notes: <number>

## Slide 16
References
MRTG: http://oss.oetiker.ch/mrtg/
RRDTool: http://oss.oetiker.ch/rrdtool/
“man rrdtool” – a good read!
Make Tobis’ day: http://tobi.oetiker.ch/wish/
Smokeping http://oss.oetiker.ch/smokeping/
Cacti http://www.cacti.net/
Nagios http://www.nagios.org/