## Slide 1: Introduction to Networking Monitoring and Management
APRICOT 2010
Kuala Lumpur, Malaysia

## Slide 2
This is a big topic...
There are a lot of tools to choose from:
  Open Source
  Commercial
  Linux/Unix-based
  Windows-based
  Network Vendor tools (Cisco, Juniper, others)
No one combination of tools is correct for everyone.
What you need to know about your network will drive your choice of tools.
Introduction

## Slide 3
System & Service monitoring
  Reachability, availability
Resource measurement/monitoring
  Capacity planning, availability
Performance monitoring (RTT, throughput)‏
Statistics & Accounting/Metering
Fault Management (Intrusion Detection)
  Fault detection, troubleshooting, and tracking
  Ticketing systems, help desk
Change management and configuration monitoring
What is network management?

## Slide 4
- Monitoring
- Data collection
- Accounting
- Capacity planning
- Availability (SLAs)‏
- Trends
- Detect problems
- Change control & monitoring
- Improvements
- Upgrades
- Fix problems
- User complaints
- Requests
- NOC Tools
- Ticket system
Ticket
Ticket
Ticket
Ticket
Ticket
Notifications
The big picture

## Slide 5
Make sure that the network is up and running. Sooooo, we need to monitor it:
  Deliver projected SLAs (Service Level Agreements)‏
  Depends on policy
    What does your management expect?
    What do your users expect?
    What do your customers expect?
    What does the rest of the Internet expect?
  Is 24x7 good enough ?
    There's no such thing as 100% uptime
Why network management?

## Slide 6
Since you have switches that support SNMP…
Use public domain tools to ping every switch and router in your network and report that back to you
  Nagios http://nagios.org/
  Sysmon http://www.sysmon.org/
  Open NMS http://www.opennms.org/
Goal is to know your network is having problems before the users start calling.
Why network management?

## Slide 7
What does it take to deliver 99.9 % uptime?
  30.5 x 24 = 762 hours a month
  (762 – (762 x .999)) x 60 = 45 minutes only of downtime a month!
Need to shutdown 1 hour / week?
  (762 - 4) / 762 x 100 = 99.4 %
  Remember to take planned maintenance into account in your calculations, and inform your users/customers if they are included/excluded in the SLA
How is availability measured?
  In the core? End-to-end? From the Internet?
Why network management?

## Slide 8
Know when to upgrade
  Is your bandwidth usage too high?
  Where is your traffic going?
  Do you need to get a faster line, or more providers?
  Is the equipment too old?
Keep an audit trace of changes
  Record all changes
  Makes it easier to find cause of problems due to upgrades and configuration changes
Where to consolidate all these functions?
  In the Network Operation Center (NOC)‏
Why network management?

## Slide 9
Where it all happens
  Coordination of tasks
  Status of network and services
  Fielding of network-related incidents and complaints
  Where the tools reside (”NOC server”)‏
  Documentation including:
    Network diagrams
    database/flat file of each port on each switch
    Network description
    Much more as you'll see a bit later.
The Network Operations Center (NOC)

## Slide 10
Maybe you’ve asked, “How do you keep track of it all?”...
...In the end, ”we” wrote our own software...
Netdot!
Documentation

## Slide 11
Basics, such as documenting your switches...
  What is each port connected to?
  Can be simple text file with one line for every port in a switch:
    health-switch1, port 1, Room 29 – Director’s office
    health-switch1, port 2, Room 43 – Receptionist
    health-switch1, port 3, Room 100 – Classroom
    health-switch1, port 4, Room 105 – Professors Office
    …..
    health-switch1, port 25, uplink to health-backbone
  This information might be available to your network staff, help desk staff, via a wiki, software interface, etc.
  Remember to label your ports!
Documentation

## Slide 12
Nice…
Documentation: Labeling

## Slide 13
There are some other Open Source network documentaiton projects, including:
to manage DHCP and DNS entries.
  See http://maintainproject.osuosl.org/about for a humorous history.
Netdisco:
    Locate a machine on the network by MAC or IP and show the switch port it lives at.
    Turn Off a switch port while leaving an audit trail. Admins log why a port was shut down.
    Inventory your network hardware by model, vendor, switch-card, firmware and operating system.
    Report on IP address and switch port usage: historical and current.
    Pretty pictures of your network.
is a web based, multilingual, TCP IP address management (IPAM) software and tracking tool.
Documentation: Software Discovery

## Slide 14
Documentation: Diagrams

## Slide 15
Windows Diagramming Software
Visio: http://office.microsoft.com/en-us/visio/FX100487861033.aspx
Ezdraw: http://www.edrawsoft.com/
Open Source Diagramming Software
Dia: http://live.gnome.org/Dia
Cisco reference icons: http://www.cisco.com/web/about/ac50/ac47/2.html
Nagios Exchange: http://www.nagiosexchange.org/
Documentation: Diagramming Software

## Slide 16
Three kinds of tools
  Diagnostic tools – used to test connectivity, ascertain that a location is reachable, or a device is up – usually active tools
  Monitoring tools – tools running in the background (”daemons” or services), which collect events, but can also initiate their own probes (using diagnostic tools), and recording the output, in a scheduled fashion.
  Performance tools – tell us how our network is handling traffic flow.
Network monitoring systems & tools

## Slide 17
Performance Tools
  Key is to look at each router interface (probably don’t need to look at switch ports).
Two common tools:
  Netflow/NfSen: http://nfsen.sourceforge.net/
  MRTG: http://oss.oetiker.ch/mrtg/
MRTG = “Multi Router Traffic Grapher”
Network monitoring systems & tools

## Slide 18
Active tools
  Ping – test connectivity to a host
  Traceroute – show path to a host
  MTR – combination of ping + traceroute
  SNMP collectors (polling)
Passive tools
  log monitoring, SNMP trap receivers, NetFlow
Automated tools
  SmokePing – record and graph latency to a set of hosts, using ICMP (Ping) or other protocols
  MRTG/RRD – record and graph bandwidth usage on a switch port or network link, at regular intervals
Network monitoring systems & tools

## Slide 19
Network & Service Monitoring tools
  Nagios – server and service monitor
    Can monitor pretty much anything
    HTTP, SMTP, DNS, Disk space, CPU usage, ...
    Easy to write new plugins (extensions)‏
  Basic scripting skills are required to develop simple monitoring jobs – Perl, Shell scripts, php, etc...
  Many good Open Source tools
    Zabbix, ZenOSS, Hyperic, ...
Use them to monitor reachability and latency in your network
  Parent-child dependency mechanisms are very useful!
Network monitoring systems & tools

## Slide 20
Monitor your critical Network Services
  DNS/Web/Email
  Radius/LDAP/SQL
  SSH to routers
How will you be notified?
Don't forget log collection!
  Every network device (and UNIX and Windows servers as well) can report system events using syslog
  You MUST collect and monitor your logs!
  Not doing so is one of the most common mistakes when doing network monitoring
Network monitoring systems & tools

## Slide 21
SNMP – Simple Network Management Protocol
  Industry standard, hundreds of tools exist to exploit it
  Present on any decent network equipment
    Network throughput, errors, CPU load, temperature, ...
  UNIX and Windows implement this as well
    Disk space, running processes, ...
SSH and telnet
  It is also possible to use scripting to automate monitoring of hosts and services
Network management protocols

## Slide 22
Net SNMP tool set
  http://net-snmp.sourceforge.net/
Very simple to build simple tools
  One that builds snapshots of which IP is used by which Ethernet address
  Another that builds shapshots of which Ethernet addresses exist on which port on which switch.
  Query remote RAID array for state.
  Query server, switches and routers for temperatures.
  Etc…
SNMP tools

## Slide 23
Traffic accounting and analysis
  What is your network used for, and how much
  Useful for Quality of Service, detecting abuses, and billing (metering)‏
  Dedicated protocol: NetFlow
  Identify traffic ”flows”: protocol, source, destination, bytes
  Different tools exist to process the information
    Flowtools, flowc
    NFSen
    ...
Statistics and accounting tools

## Slide 24
Is the problem transient?
  Overload, temporary resource shortage
Is the problem permanent?
  Equipment failure, link down
How do you detect an error?
  Monitoring!
  Customer complaints
A ticket system is essential
  Open ticket to track an event (planned or failure)‏
  Define dispatch/escalation rules
    Who handles the problem?
    Who gets it next if no one is available?
Fault and problem management

## Slide 25
Why are they important?
  Track all events, failures and issues
Focal point for helpdesk communication
Use it to track all communications
  Both internal and external
Events originating from the outside:
  customer complaints
Events originating from the inside:
  System outages (direct or indirect)‏
  Planned maintenances or upgrades – Remember to notify your customers!
Ticketing systems

## Slide 26
Use ticket system to follow each case, including internal communication between technicians
Each case is assigned a case number
Each case goes through a similar life cycle:
  New
  Open
  ...
  Resolved
  Closed
Ticketing systems

## Slide 27
Workflow: Ticket System Helpdesk Tech Eqpt ---------------------------------------------------------------- T T T T query | | | | from ---->| | | | customer |--- request --->| | | <- ack. -- | | | | | |<-- comm --> | | | | |- fix issue -> eqpt | |<- report fix -| | customer <-|<-- respond ----| | | | | | |
Ticketing systems

## Slide 28
rt (request tracker)
  Heavily used worldwide.
  A classic ticketing system that can be customized to your location.
  Somewhat difficult to install and configure.
  Handles large-scale operations.
trac
  A hybrid system that includes a wiki and project management features.
  Ticketing system is not as robust as rt, but works well.
  Often used for ”trac”king group projects.
redmine
  Like trac, but more robust. Harder to install
Ticketing systems: examples

## Slide 29
These are systems that observe all of your network traffic and report when it sees specific kinds of problems, such as:
  hosts that are infected or are acting as spamming sources.
A few tools:
  SNORT - a commonly used open source tool: http://www.snort.org/
  Prelude – Security Information Management System https://dev.prelude-technologies.com/
  Samhain – Centralized HIDS http://la-samhna.de/samhain/
  Nessus - scan for vulnerabilities: http://www.nessus.org/download/
Network Intrusion Detection Systems (NIDS)

## Slide 30
Record changes to equipment configuration using revision control (also for configuration files)‏
Inventory management (equipment, IPs, interfaces)
Use versioning control
  As simple as: ”cp named.conf named.conf.20070827-01”
For plain configuration files:
  CVS, Subversion (SVN)
  Mercurial
For routers:
  RANCID
Configuration management and monitoring

## Slide 31
Traditionally, used for source code (programs)
Works well for any text-based configuration files
  Also for binary files, but less easy to see differences
For network equipment:
  RANCID (Automatic Cisco configuration retrieval and archiving, also for other equipment types)
Built-in to Project Management Software like:
  Trac
  Redmine
  And, many other wiki products. Excellent for documenting your network.
Configuration management and monitoring

## Slide 32
- Monitoring
- Data collection
- Accounting
- Capacity planning
- Availability (SLAs)‏
- Trends
- Detect problems
- Change control & monitoring
- Improvements
- Upgrades
- Fix problems
- User complaints
- Requests
- NOC Tools
- Ticket system
Ticket
Ticket
Ticket
Ticket
Ticket
Notifications
The big picture revisited

## Slide 33
Performance
Cricket
IFPFM
flowc
mrtg
netflow
NfSen
ntop
pmacct
rrdtool
SmokePing
SNMP/Perl/ping
Ticketing
RT, Trac, Redmine
Net Management
Big Brother
Big Sister
Cacti
Hyperic
Munin
Nagios*
Netdisco
Netdot
OpenNMS
Sysmon
Zabbix
Change Mgmt
Mercurial
Rancid (routers)
RCS
Subversion
Security/NIDS
Nessus
OSSEC
Prelude
Samhain
SNORT
Untangle
A few Open Source solutions…

## Slide 34
Questions?
?