## Slide 1: Cisco Configuration Elements
APRICOT 2010
Kuala Lumpur, Malaysia

## Slide 2
Overview
Basic things that we need to make sure are configured on a Cisco router (and switch) to do proper network management
These apply to other network equipment manufacturers of course, and to servers and workstations
Notes: <number>

## Slide 3
Hostname: Hostname of the device
SSH: Enable Secure SHell
DNS: Domain Name Lookup
NTP: Time synchronization
(Network Time Protocol)
Syslog: System log messages
SNMP: SNMP configuration
SNMP traps: Where to send traps
CDP: Cisco Discovery Protocol
Elements
Notes: <number>

## Slide 4
Access the router
ssh user@router
You are in “user mode” rtr>
If you’re user has the privileges, go to “privileged mode” rtr>enable (might need pw) rtr#conf t rtr(config)#
Type in configuration commands.
Exit and save/build your new configuration rtr(config)#exit rtr#wr mem

## Slide 5
Preferably we use the FQDN (Fully Qualified Domain Name).
In config mode on the router rtr(config)#hostname net-gw.XYZ.domain.name or rtr(config)#hostname net-sw-XYZ.domain.name
Hostname
Notes: <number>

## Slide 6
In config mode on the router: ip domain-name .mgmt.conference.apricot.net ip name-server 169.223.142.3
DNS configuration
Notes: <number>

## Slide 7
In config mode: ntp server pool.ntp.org clock timezone EEST 3
If needed: clock summer-time XXX recurring \ last Sun Mar 2:00 last Sun Oct \ 3:00
Verify: rtr>show clock
NTP + time configuration
Notes: <number>

## Slide 8
Only crypto version of IOS/CatOS have support for SSH – there are export restrictions... In config mode: rtr#aa new-model rtr#crypto key generate rsa rtr#username inst secret 0 xxxxxx
…above is required to be allowed to enable SSH. Verify creation with: sh crypto key mypubkey rsa
Use at least 768 bits - OpenSSH requires it
SSH
Notes: <number>

## Slide 9
Enforce ssh (disabling telnet) on vty lines rtr#conf t rtr(config)#line vty 0 4 rtr(config)#transport input ssh rtr(config)#^Z (“exit” completely) rtr#wr mem
SSH is now enabled
Telnet is not necessary disabled!
  Use ACLs to be sure of this
SSH continued
Notes: <number>

## Slide 10
In config mode, enable logging to your NOC machine (X is your network) rtr(config)#logging 192.168.X.1 rtr(config)#logging facility local5 rtr(config)#logging trap debugging
Syslog
Notes: <number>

## Slide 11
In config mode: # snmp-server community xxxxxxxxx RW # snmp-server community public RO # snmp-server location KL # snmp-server enable traps config # snmp-server enable traps envmon # snmp-server enable traps config-copy # snmp-server enable traps syslog # snmp-server host 169.223.142.x public
SNMP
Notes: <number>

## Slide 12
Cisco Discovery Protocol
Enabled by default nowadays in current IOS versions.
Otherwise, enable with ”cdp enable” or ”cdp run” in configure mode on your router.
tcpdump and tools like cdpr will show you CDP announcements
check neighbor announcement with: rtr>show cdp neighbors
CDP
Notes: <number>

## Slide 13
?
Questions?
Notes: <number>