## Slide 1: NetFlow
Network Management Workshop
APRICOT 2010
Kuala Lumpur

## Slide 2: Contents
Netflow
  What it is and how it works
  Uses and Applications
Vendor Configurations/Implementation
  Cisco and Juniper
NetFlow tools
  Architectural issues
  Software, tools etc

## Slide 3: What are Network Flows ?
Packets or frames that have a common attribute.
Creation and expiration policy – what conditions start and stop a flow.
Counters – packets,bytes,time.
Routing information – AS, network mask, interfaces.

## Slide 4: Network Flows...
Unidirectional or bidirectional.
Bidirectional flows can contain other information such as round trip time, TCP behavior.
Application flows look past the headers to classify packets by their contents.
Aggregated flows – flows of flows.

## Slide 5: Unidirectional Flow with Source/Destination IP Key
10.0.0.1
10.0.0.2
% telnet 10.0.0.2
login:
Active Flows
Flow Source IP Destination IP
1 10.0.0.1 10.0.0.2
2 10.0.0.2 10.0.0.1

## Slide 6: Unidirectional Flow with Source/Destination IP Key
10.0.0.1
10.0.0.2
% telnet 10.0.0.2
login:
Active Flows
Flow Source IP Destination IP
1 10.0.0.1 10.0.0.2
2 10.0.0.2 10.0.0.1
% ping 10.0.0.2
ICMP echo reply

## Slide 7: Unidirectional Flow with IP, Port,Protocol Key
10.0.0.1
10.0.0.2
login:
Active Flows
Flow Source IP Destination IP prot srcPort dstPort
1 10.0.0.1 10.0.0.2 TCP 32000 23
2 10.0.0.2 10.0.0.1 TCP 23 32000
3 10.0.0.1 10.0.0.2 ICMP 0 0
4 10.0.0.2 10.0.0.1 ICMP 0 0
% telnet 10.0.0.2
% ping 10.0.0.2
ICMP echo reply

## Slide 8: Bidirectional Flow with IP, Port,Protocol Key
10.0.0.1
10.0.0.2
% telnet 10.0.0.2
login:
Active Flows
Flow Source IP Destination IP prot srcPort dstPort
1 10.0.0.1 10.0.0.2 TCP 32000 23
2 10.0.0.1 10.0.0.2 ICMP 0 0
% ping 10.0.0.2
ICMP echo reply

## Slide 9: Application Flow
10.0.0.1
10.0.0.2
% firefox http://10.0.0.2:9090
Content-type:
Active Flows
Flow Source IP Destination IP Application
1 10.0.0.1 10.0.0.2 HTTP
Web server on
Port 9090

## Slide 10: Aggregated Flow
Flow Source IP Destination IP prot srcPort dstPort
1 10.0.0.1 10.0.0.2 TCP 32000 23
2 10.0.0.2 10.0.0.1 TCP 23 32000
3 10.0.0.1 10.0.0.2 ICMP 0 0
4 10.0.0.2 10.0.0.1 ICMP 0 0
Source/Destination IP Aggregate
Flow Source IP Destination IP
1 10.0.0.1 10.0.0.2
2 10.0.0.2 10.0.0.1
Main Active flow table

## Slide 11: Working with Flows
Generating and Viewing Flows
Exporting Flows from devices
  Types of flows
  Sampling rates
Collecting it
  Tools to Collect Flows - Flow-tools
Analyzing it
  Use existing or write your own

## Slide 12: Flow Descriptors
A Key with more elements will generate more flows.
Greater number of flows leads to more post processing time to generate reports, more memory and CPU requirements for device generating flows.
Depends on application. Traffic engineering vs. intrusion detection.

## Slide 13: Flow Accounting
Accounting information accumulated with flows.
Packets, Bytes, Start Time, End Time.
Network routing information – masks and autonomous system number.

## Slide 14: Flow Generation/Collection
Passive monitor
  A passive monitor (usually a unix host) receives all data and generates flows.
  Resource intensive, newer investments needed
Router or other existing network device.
  Router or other existing devices like switch, generate flows.
  Sampling is possible
  Nothing new needed

## Slide 15: Passive Monitor Collection
Workstation A
Workstation B
Campus
Flow probe connected
to switch port in
“ traffic mirror” mode

## Slide 16: Router Collection
Flow collector
stores exported flows from router.
LAN
LAN
LAN
Internet
LAN

## Slide 17: Passive Monitor
Directly connected to a LAN segment via a switch port in “mirror” mode, optical splitter, or repeated segment.
Generate flows for all local LAN traffic.
Must have an interface or monitor deployed on each LAN segment.
Support for more detailed flows – bidirectional and application.

## Slide 18: Router Collection
Router will generate flows for traffic that is directed to the router.
Flows are not generated for local LAN traffic.
Limited to “simple” flow criteria (packet headers).
Generally easier to deploy – no new equipment.

## Slide 19: Vendor implementations

## Slide 20: Cisco NetFlow
Unidirectional flows.
IPv4 unicast and multicast.
Aggregated and unaggregated.
Flows exported via UDP.
Supported on IOS and CatOS platforms.
Catalyst NetFlow is different from IOS

## Slide 21: Cisco NetFlow Versions
4 Unaggregated types (1,5,6,7).
14 Aggregated types (8.x, 9).
Each version has its own packet format.
Version 1 does not have sequence numbers – no way to detect lost flows.
The “version” defines what type of data is in the flow.
Some versions specific to Catalyst platform.

## Slide 22: NetFlow v1
Key fields: Source/Destination IP, Source/Destination Port, IP Protocol, ToS, Input interface.
Accounting: Packets, Octets, Start/End time, Output interface
Other: Bitwise OR of TCP flags.

## Slide 23: NetFlow v5
Key fields: Source/Destination IP, Source/Destination Port, IP Protocol, ToS, Input interface.
Accounting: Packets, Octets, Start/End time, Output interface.
Other: Bitwise OR of TCP flags, Source/Destination AS and IP Mask.
Packet format adds sequence numbers for detecting lost exports.

## Slide 24: NetFlow v8
Aggregated v5 flows.
Not all flow types available on all equipments
Much less data to post process, but loses fine granularity of v5 – no IP addresses.

## Slide 25: NetFlow v8
AS
Protocol/Port
Source Prefix
Destination Prefix
Prefix
Destination
Source/Destination
Full Flow

## Slide 26: NetFlow v8
ToS/AS
ToS/Protocol/Port
ToS/Source Prefix
ToS/Destination Prefix
Tos/Source/Destination Prefix
ToS/Prefix/Port

## Slide 27: NetFlow v9
Record formats are defined using templates.
Template descriptions are communicated from the router to the NetFlow Collection Engine.
Flow records are sent from the router to the NetFlow Collection Engine with minimal template information so that the NetFlow Collection Engine can relate the records to the appropriate template.
Version 9 is independent of the underlying transport (UDP, TCP, SCTP, and so on).

## Slide 28: NetFlow Packet Format
Common header among export versions.
All but v1 have a sequence number.
Version specific data field where N records of data type are exported.
N is determined by the size of the flow definition. Packet size is kept under ~1480 bytes. No fragmentation on Ethernet.

## Slide 29: NetFlow v5 Packet Example
NetFlow
v5 header
v5 record
IP/UDP packet
v5 record
…
…

## Slide 30: NetFlow v5 Packet (Header)‏
struct ftpdu_v5 {
/* 24 byte header */
u_int16 version; /* 5 */
u_int16 count; /* The number of records in the PDU */
u_int32 sysUpTime; /* Current time in millisecs since router booted */
u_int32 unix_secs; /* Current seconds since 0000 UTC 1970 */
u_int32 unix_nsecs; /* Residual nanoseconds since 0000 UTC 1970 */
u_int32 flow_sequence; /* Seq counter of total flows seen */
u_int8 engine_type; /* Type of flow switching engine (RP,VIP,etc.) */
u_int8 engine_id; /* Slot number of the flow switching engine */
u_int16 reserved;

## Slide 31: NetFlow v5 Packet (Records)‏
/* 48 byte payload */
struct ftrec_v5 {
u_int32 srcaddr; /* Source IP Address */
u_int32 dstaddr; /* Destination IP Address */
u_int32 nexthop; /* Next hop router's IP Address */
u_int16 input; /* Input interface index */
u_int16 output; /* Output interface index */
u_int32 dPkts; /* Packets sent in Duration */
u_int32 dOctets; /* Octets sent in Duration. */
u_int32 First; /* SysUptime at start of flow */
u_int32 Last; /* and of last packet of flow */
u_int16 srcport; /* TCP/UDP source port number or equivalent */
u_int16 dstport; /* TCP/UDP destination port number or equiv */
u_int8 pad;
u_int8 tcp_flags; /* Cumulative OR of tcp flags */
u_int8 prot; /* IP protocol, e.g., 6=TCP, 17=UDP, ... */
u_int8 tos; /* IP Type-of-Service */
u_int16 src_as; /* originating AS of source address */
u_int16 dst_as; /* originating AS of destination address */
u_int8 src_mask; /* source address prefix mask bits */
u_int8 dst_mask; /* destination address prefix mask bits */
u_int16 drops;
} records[FT_PDU_V5_MAXFLOWS];
};

## Slide 32: NetFlow v8 Packet Example (AS Aggregation)‏
NetFlow
v8 header
v8 record
IP/UDP packet
v8 record
…
…

## Slide 33: NetFlow v8 AS agg. Packet
struct ftpdu_v8_1 {
/* 28 byte header */
u_int16 version; /* 8 */
u_int16 count; /* The number of records in the PDU */
u_int32 sysUpTime; /* Current time in millisecs since router booted */
u_int32 unix_secs; /* Current seconds since 0000 UTC 1970 */
u_int32 unix_nsecs; /* Residual nanoseconds since 0000 UTC 1970 */
u_int32 flow_sequence; /* Seq counter of total flows seen */
u_int8 engine_type; /* Type of flow switching engine (RP,VIP,etc.) */
u_int8 engine_id; /* Slot number of the flow switching engine */
u_int8 aggregation; /* Aggregation method being used */
u_int8 agg_version; /* Version of the aggregation export */
u_int32 reserved;
/* 28 byte payload */
struct ftrec_v8_1 {
u_int32 dFlows; /* Number of flows */
u_int32 dPkts; /* Packets sent in duration */
u_int32 dOctets; /* Octets sent in duration */
u_int32 First; /* SysUpTime at start of flow */
u_int32 Last; /* and of last packet of flow */
u_int16 src_as; /* originating AS of source address */
u_int16 dst_as; /* originating AS of destination address */
u_int16 input; /* input interface index */
u_int16 output; /* output interface index */
} records[FT_PDU_V8_1_MAXFLOWS];
};

## Slide 34: Cisco IOS Configuration
Configured on each input interface.
Define the version.
Define the IP address of the collector (where to send the flows).
Optionally enable aggregation tables.
Optionally configure flow timeout and main (v5) flow table size.
Optionally configure sample rate.

## Slide 35: Cisco IOS Configuration
interface FastEthernet0/0
description Access to backbone
ip address 169.223.132.10 255.255.255.0
ip flow egress
ip flow ingress
duplex auto
speed auto
!
interface FastEthernet0/1
description Access to local net
ip address 169.223.142.1 255.255.255.224
duplex auto
speed auto
ip flow-export version 5
ip flow-export destination 169.223.142.3 2002
ip flow top-talkers
top 10
sort-by bytes

## Slide 36: Cisco IOS Configuration
IOS versions
interface FastEthernet0/0
ip route-cache flow ! Prior to IOS 12.4
ip flow [ingress|egress] ! From IOS 12.4

## Slide 37: Cisco IOS Configuration
Flow export v5 is enabled for main cache
Exporting flows to 169.223.142.3 (2002)
Exporting using source IP address 169.223.142.1
Version 5 flow records
127480 flows exported in 6953 udp datagrams
0 flows failed due to lack of export packet
0 export packets were sent up to process level
0 export packets were dropped due to no fib
0 export packets were dropped due to adjacency issues
0 export packets were dropped due to fragmentation failures
0 export packets were dropped due to encapsulation fixup failures

## Slide 38: Cisco IOS Configuration
bb-gw#sh ip cache flow
IP packet size distribution (1765988 total packets):
1-32 64 96 128 160 192 224 256 288 320 352 384 416 448 480
.000 .538 .113 .049 .027 .006 .002 .006 .002 .001 .001 .001 .017 .002 .001
512 544 576 1024 1536 2048 2560 3072 3584 4096 4608
.001 .001 .002 .018 .204 .000 .000 .000 .000 .000 .000
IP Flow Switching Cache, 278544 bytes
105 active, 3991 inactive, 127794 added
2151823 ager polls, 0 flow alloc failures
Active flows timeout in 30 minutes
Inactive flows timeout in 15 seconds
IP Sub Flow Cache, 21640 bytes
105 active, 919 inactive, 127726 added, 127726 added to flow
0 alloc failures, 0 force free
1 chunk, 8 chunks added
last clearing of statistics never
Protocol Total Flows Packets Bytes Packets Active(Sec) Idle(Sec)
-------- Flows /Sec /Flow /Pkt /Sec /Flow /Flow
TCP-Telnet 62 0.0 60 50 0.0 15.7 14.3
TCP-FTP 1 0.0 3 60 0.0 8.9 15.2
TCP-WWW 54359 0.1 14 658 2.3 5.3 5.1
TCP-SMTP 20 0.0 103 47 0.0 6.3 13.5
...

## Slide 39: Cisco IOS Configuration
TCP-X 1991 0.0 32 40 0.1 0.5 14.3
TCP-other 8069 0.0 61 214 1.5 7.8 8.9
UDP-DNS 24371 0.0 1 69 0.0 0.1 15.4
UDP-NTP 7208 0.0 1 74 0.0 0.0 15.4
UDP-Frag 14 0.0 1 508 0.0 1.2 15.4
UDP-other 27261 0.0 11 105 0.9 0.4 15.4
ICMP 4457 0.0 17 83 0.2 16.9 15.4
IP-other 1 0.0 1 50 0.0 0.0 15.6
Total: 128017 0.3 13 373 5.3 3.5 10.6
SrcIf SrcIPaddress DstIf DstIPaddress Pr SrcP DstP Pkts
Fa0/0 210.118.80.41 Fa0/1 169.223.142.112 11 0627 059A 1
Fa0/1 169.223.142.3 Fa0/0* 169.223.35.48 06 0050 C166 1
Fa0/0 169.223.35.175 Local 169.223.142.1 06 EFFD 0016 145
Fa0/0 169.223.35.175 Local 169.223.142.1 06 EFFC 0017 1
Fa0/0 169.223.35.175 Fa0/1 169.223.142.3 06 EE61 0016 79
Fa0/1 169.223.142.102 Fa0/0* 216.34.181.71 06 E058 0050 6
Fa0/1 169.223.142.70 Fa0/0* 66.220.146.18 06 CBD3 0050 6
Fa0/0 208.81.191.110 Fa0/1 169.223.142.70 06 0050 DABD 13
…

## Slide 40: Cisco IOS Configuration
ip flow-top-talkers
top 10
sort-by bytes
bb-gw#show ip flow top-talkers
SrcIf SrcIPaddress DstIf DstIPaddress Pr SrcP DstP Bytes
Fa0/1 169.223.142.39 Fa0/0* 169.223.35.139 06 0050 D804 33K
Fa0/0 169.223.32.102 Fa0/1 169.223.142.37 06 816E 0016 28K
Fa0/1 169.223.142.39 Fa0/0* 169.223.35.139 06 0050 D805 26K
Fa0/1 169.223.142.39 Fa0/0* 169.223.35.139 06 0050 D807 24K
Fa0/1 169.223.142.39 Fa0/0* 169.223.35.139 06 0050 D806 23K
Fa0/1 169.223.142.37 Fa0/0* 169.223.32.102 06 0016 816E 23K
Fa0/0 169.223.35.139 Fa0/1 169.223.142.39 06 D804 0050 6675
Fa0/1 169.223.142.70 Fa0/0* 208.81.191.110 06 ABE7 0050 4341
Fa0/0 169.223.35.175 Fa0/1 169.223.142.3 06 EE61 0016 3140
Fa0/1 169.223.142.3 Fa0/0* 169.223.35.175 06 0016 EE61 2528
10 of 10 top talkers shown. 122 flows processed.

## Slide 41: Cisco command summary
Enable flow on each interface
ip route-cache flow
OR
ip flow ingress
ip flow egress
View flows
  show ip cache flow
  show ip flow top-talkers

## Slide 42: Cisco Command Summary
Export flows
ip flow-export version 5 [origin-as|peer-as]
ip flow-export destination x.x.x.x <udp-port>
Exporting aggregated flows
ip flow-aggregation cache as|prefix|dest|source|proto
enabled
export destination x.x.x.x <udp-port>

## Slide 43: Flows and Applications

## Slide 44: Uses for Flow
Problem identification / solving
  Traffic classification
  DoS Traceback (some slides by Danny McPherson)‏
Traffic Analysis
  Inter-AS traffic analysis
  Reporting on application proxies
Accounting
  Cross verification from other sources
  Can cross-check with SNMP data

## Slide 45: Traffic Classification
Based on Protocol, source and destination ports
  Protocol identification (TCP, UDP, ICMP)‏
  Can define well known ports
  Can identify well known P2P ports
  Most common use
    Proxy measurement - http , ftp
    Rate limiting P2P traffic

## Slide 46: Traceback: Flow-based*
Trace attack by matching fingerprint/signature at each interface via passive monitoring:
  Flow data (e.g., NetFlow, cflowd, sFlow, IPFIX)‏
  Span Data
  PSAMP (Packet Sampling, IETF PSAMP WG)‏
Number of open source and commercial products evolving in market
Non-intrusive, widely supported

## Slide 47: Flow-based Detection*
Monitor flows (i.e., Network and Transport Layer transactions) on the network and build baselines for what normal behavior looks like:
  Per interface
  Per prefix
  Per Transport Layer protocol & ports
  Build time-based buckets (e.g., 5 minutes, 30 minutes, 1 hours, 12 hours, day of week, day of month, day of year)‏

## Slide 48: Detect Anomalous Events: SQL “Slammer” Worm*

## Slide 49: Flow-based Detection (cont)*
Once baselines are built anomalous activity can be detected
  Pure rate-based (pps or bps) anomalies may be legitimate or malicious
  Many misuse attacks can be immediately recognized, even without baselines (e.g., TCP SYN or RST floods)‏
  Signatures can also be defined to identify “interesting” transactional data (e.g., proto udp and port 1434 and 404 octets(376 payload) == slammer!)‏
  Temporal compound signatures can be defined to detect with higher precision

## Slide 50: Flow-based Commercial Tools…*

## Slide 51: Commercial Detection A Large Scale DOS attack*

## Slide 52: Traceback: Commercial*

## Slide 53: Commercial Traceback: More Detail*

## Slide 54: Traffic Analysis
Can see traffic based on source and destination AS
  Source and destination AS derived through the routing table on the router
  Introduces the need to run full mesh BGP at IXPs as well as transit and peering
  Source and destination prefix based flows can be collected and plotted against external prefix to ASN data

## Slide 55: Accounting
Flow based accounting can be a good supplement to SNMP based accounting.

## Slide 56: SNMP and Flows
Data Courtesy AARNET, Australia and Bruce Morgan

## Slide 57: See the fine lines..
Data Courtesy AARNET, Australia and Bruce Morgan

## Slide 58: SNMP and Flows
Data Courtesy AARNET, Australia and Bruce Morgan

## Slide 59: What Next
IPFIX (IP Flow Information Exchange)‏
  To make the flow format uniform and make it easier to write analysis tools
  http://www1.ietf.org/html.charters/ipfix-charter.html
  Requirements for IP Flow Information Export (RFC 3917)
  Evaluation of Candidate Protocols for IP Flow Information Export (IPFIX) (RFC 3955)‏

## Slide 60: References
flow-tools: http://www.splintered.net/sw/flow-tools
NetFlow Applications http://www.inmon.com/technology/netflowapps.php
Netflow HOW-TO http://www.linuxgeek.org/netflow-howto.php
IETF standards effort: http://www.ietf.org/html.charters/ipfix-charter.html

## Slide 61: References
Abilene NetFlow page http://abilene-netflow.itec.oar.net/
Flow-tools mailing list: flow-tools@splintered.net
Cisco Centric Open Source Community http://cosi-nms.sourceforge.net/related.html

## Slide 62: References
http://ensight.eos.nasa.gov/FlowViewer/
http://nfsen.sourceforge.net/
http://www.netflowdashboard.com/