## Slide 1: Log management
Network Management Workshop
APRICOT 2010
Kuala Lumpur

## Slide 2: Log management and monitoring
What is log management and monitoring ?
It's about keeping your logs in a safe place, putting them where you can easily inspect them with tools
Keep an eye on your log files
They tell you something important...
  Lots of things happen, and someone needs to keep an eye on them...
  Not really practictal to do it by hand!

## Slide 3: Log management and monitoring
On your routers and switches
  Sep 1 04:40:11.788 INDIA: %SEC-6-IPACCESSLOGP: list 100 denied tcp 79.210.84.154(2167) -> 169.223.192.85(6662), 1 packet
  Sep 1 04:42:35.270 INDIA: %SYS-5-CONFIG_I: Configured from console by pr on vty0 (203.200.80.75)
  %CI-3-TEMP: Overtemperature warning
  Mar 1 00:05:51.443: %LINK-3-UPDOWN: Interface Serial1, changed state to down
On your servers as well
  Aug 31 17:53:12 ubuntu nagios3: Caught SIGTERM, shutting down...
  Aug 31 19:19:36 ubuntu sshd[16404]: Failed password for root from 169.223.1.130 port 2039 ssh2

## Slide 4: Log management
First, need to centralize and consolidate log files
Log all messages from routers, switches and servers to a single machine – a logserver
All logging from network equipment and UNIX servers is done using syslog
Windows can be configured to use syslog as well, with some tools
Log locally, but also to the central server

## Slide 5: Centralized logging
Local disk
server
syslog
router
switch
Syslog storage
Syslog
server

## Slide 6: Configuring centralized logging
Cisco equipment
  Minimum:
    logging ip.of.log.host
UNIX host
  Edit /etc/syslog.conf, and add:
  *.* @ip.of.log.host
  Restart syslogd
Other equipments have similar options
  Options to control facility and level

## Slide 7: Receiving the messages
Identify the facility that the SENDING host or device will send their message on
Reconfigure syslogd to listen to the network (on Ubuntu/Debian: add ”-r” to /etc/defaults/syslogd
Add an entry to syslogd indicating where to write messages: local7.* /var/log/routers
Create the file: touch /var/log/routers
Restart syslogd /etc/init.d/sysklogd restart

## Slide 8: Syslog basics
UDP protocol, port 514
Syslog messages have two attributes (other than the message itself):
Facility Level Auth Security | Emergency (0) Authpriv User | Alert (1) Console Syslog | Critical (2) Cron UUCP | Error (3) Daemon Mail | Warning (4) Ftp Ntp | Notice (5) Kern News | Info (6) Lpr | Debug (7) Local0 ...Local7 |

## Slide 9: Sorting logs
Using facility and level, sort by category into different files
With tools like syslog-ng, sort by host, date, ... automatically into different directories
Grep your way through the logs.
Use standard UNIX tools to sort, and eliminate, things you want to filter out:
  egrep -v '(list 100 denied|logging rate-limited)' mylogfile
  Is there a way to do this automatically ?

## Slide 10: SWATCH
Simple Log Watcher
  Written in Perl
  Monitors log files, looking for patterns (”regular expressions”) to match in the logs
  Perform a given action if the pattern is found

## Slide 11: Sample config
ignore /things to ignore/
watchfor /NATIVE_VLAN_MISMATCH/
mail=root,subject=VLAN problem
threshold type=limit,count=1,seconds=3600
watchfor /CONFIG_I/
mail=root,subject=Router config
threshold type=limit,count=1,seconds=3600

## Slide 12: References
http://www.loganalysis.org/
Syslog NG
  http://www.balabit.com/network-security/syslog-ng/
Windows Event Log to Syslog:
  https://engineering.purdue.edu/ECN/Resources/Documents/UNIX/evtsys
SWATCH log watcher
  http://swatch.sourceforge.net/
  http://www.loganalysis.org/sections/signatures/log-swatch-skendrick.txt
  http://www.loganalysis.org/
  http://sourceforge.net/docman/display_doc.php?docid=5332&group_id=25401

## Slide 13: References
http://www.crypt.gen.nz/logsurfer/
http://sial.org/howto/logging/swatch/
http://www.occam.com/sa/CentralizedLogging2009.pdf
http://ristov.users.sourceforge.net/slct/

## Slide 14: Questions ?
?